## Slide 1: HERBERT Autonomous Rubik’s Cube Solver
Dylan Lytle
Li Lao
Matt Frandsen
Jon Whitaker

## Slide 2: What inspires you?
CubeStormer1 & 3 – Fastest robot to solve a Rubik’s Cube (3.253s) [1].
Zackary Gromko – Claims a new record on October 15, 2015 (2.39s) [2].
https://youtu.be/X0pFZG7j5cE
https://youtu.be/bEiQwmEe45s?t=13s
Notes: Jon

## Slide 3: Introduction
GOAL: Create an autonomous robotic Rubik's Cube solver.
Integrates various technologies
  Video cameras, stepper motors, mechanical actuators, single-board computer, FPGA
Possibly overtake Guinness World Record (3.253s at the time)
Optimize mechanical and image processing operations while maintaining the precision needed to solve the cube.
Notes: Jon

## Slide 4: High level System Diagram
Notes: Jon

## Slide 5: OpenCV & Image Processing
Notes: Li

## Slide 6: OpenCV & Image Processing
Original Plan
Two cameras, one for three of the six faces of the cube.
Grayscale conversion – Convert RGB to pixel intensity for feature filtration [3].
Canny edge detection - Identify the edges of the cube and the faces [4].
Contour filtering - Identify cubelets on each face [5].
Notes: Li

## Slide 7: OpenCV & Image Processing
Final Implementation
One camera
Static mask
Notes: Li

## Slide 8: Opencv and Image PRocessing
HSV conversion – Convert RGB to HSV [3].
HSV characterization – Use pixel histogram and bin each facelet (square) [6].
Histogram optimization

## Slide 9: Kcube & Solution Sequence
Cubelets represented with an ASCII character
  ‘W’, ‘R’, ‘B’, ‘G’, ‘O’, ‘Y’
Kcube application used to generate the solution sequence [5].
  Created by Greg Schmidt
  Utilizes Kociemba’s algorithm
Microsoft Windows [ Version X.X. XXX ]
Copyright (c) 2015 Microsoft Corporation . All rights reserved .
c:> kcube L: GGWWOWBRB F: GWGBGYWBO U: YOOOWYROY D: ORGWYYYRB R: OGBBRYWRR B: YBROBGWGR
Notes: Jon

## Slide 10: Mechanical Actuators
Notes: Dylan

## Slide 11: Mechanical Actuators
One arm for each face
  Improvement over 4 arms solutions
Each arm actuates, avoiding contact with the other arms
Original Ideas
  Rotary  Linear motion
  Linear actuator motor
Notes: Dylan

## Slide 12: Mechanical Actuators
Final Implementation
Double action pneumatic air cylinder
  High Speed
  Affordable
  Small footprint
Controlled by solenoid valve and a relay board
Simultaneous coaxial pair motion
Approximately 40-60psi
Notes: Dylan

## Slide 13: Electro-Mechanical Stepper Motors

## Slide 14: Electro-Mechanical Stepper Motors
Each actuating arm has a stepper motor to rotate each face
90/180 degree rotations clockwise or counter-clockwise
Controlled by an FPGA and proprietary motor control board
Full steps, no micro-stepping
Break sensor for 90 degree
alignment
Notes: Matt

## Slide 15: Electro-Mechanical Stepper Motors
Progression of Arm Pieces
Notes: Matt

## Slide 16: Challenges
Implementing & Synchronizing a system with 6 arm assemblies
System integration
Construction & Component acquisition
Image processing
  ROI issues
  Color characterization (lighting)
Team scheduling
Notes: Jon

## Slide 17: Summary
Integrates various technologies and domains of engineering.
  Computer and Electrical engineering combined with mechatronics and robotics
Overcame many challenges
Great application of system integration and teamwork.
Notes: Jon

## Slide 18: Acknowledgments
Point Grey Research
BioFire Defense
Futura Industries

## Slide 19: REFERENCES
[1] Guinness World Records. Fastest robot to solve a Rubik's Cube [Online]. Available: http://www.guinnessworldrecords.com/world-records/fastest-robot-to-solve-a-rubiks-cub
[2] Guinness World Records. Robot created by American student solves a Rubik’s cube in just 2.39 seconds [Online]. Available: http://www.guinnessworldrecords.com/news/2015/11/robot-created-by-american-student-solves-a-rubiks-cube-in-just-2-39-seconds
[3] OpenCV Developers Team. Miscellaneous Image Transformations [Online].
Available: http://docs.opencv.org/modules/imgproc/doc/miscellaneous_transformations.html#cvtcolor
[4] OpenCV Developers Team. Feature Detection [Online]. Available: http://docs.opencv.org/modules/imgproc/doc/feature_detection.html?highlight=canny#canny
[5] OpenCV Developers Team. Structural Analysis and Shape Descriptors [Online]. Available: http://docs.opencv.org/modules/imgproc/doc/structural_analysis_and_shape_descriptors.html?highlight=findcontours#findcontours
[6] OpenCV Developers Team. Histograms in OpenCV [Online]. Available: http://opencv-python-tutroals.readthedocs.org/en/latest/py_tutorials/py_imgproc/py_histograms/py_histogram_begins/py_histogram_begins.html