## Slide 1: HERBERT Autonomous Rubik’s Cube Solver
Dylan Lytle
Li Lao
Matt Frandsen
Jon Whitaker

## Slide 2: Background
CubeStormer 3 – Fastest robot to solve a Rubik’s Cube (3.253s) [1].

## Slide 3: Introduction
GOAL: Create an autonomous robotic Rubik's Cube solver.
Integrates various technologies
  Video cameras, stepper motors, mechanical actuators, single-board computer, FPGA
Take Guinness World Record (3.253s)
Optimize mechanical operations while maintaining the precision needed to rotate the cube.

## Slide 4
Corner
Face
Cubelet
Edge
Cubies
Cube Representation

## Slide 5
Middle Facelets Determine Face Color
(U = Orange, R = Green, F = Yellow, etc.)
8 Corner Cubies
12 Edge Cubies

## Slide 6
F
R
U
B
D
L
F
F Face Twisted Clockwise
R’
R Face Twisted Counterclockwise
U2
U Face Twisted 180 Degrees

## Slide 7: High level System Diagram

## Slide 8: OpenCV & Image Processing
Two cameras, one for three of the six faces of the cube.
Grayscale conversion – Convert RGB to pixel intensity for feature filtration [2].
Canny edge detection - Identify the edges of the cube and the faces [3].
Contour filtering - Identify cubelets on each face [4].

## Slide 9: Kcube & Solution Sequence
Cubelets represented with an ASCII character
  ‘W’, ‘R’, ‘B’, ‘G’, ‘O’, ‘Y’
Kcube application used to generate the solution sequence [5].
  Created by Greg Schmidt
  Utilizes Kociemba’s algorithm
Microsoft Windows [ Version X.X. XXX ]
Copyright (c) 2015 Microsoft Corporation . All rights reserved .
c:> kcube L: GGWWOWBRB F: GWGBGYWBO U: YOOOWYROY D: ORGWYYYRB R: OGBBRYWRR B: YBROBGWGR

## Slide 10
R
U
B
D
F’
R’
U’
F
B’
L’
D’
B2
F2
R2
U2
L2
D2
.
.
.
.
.
.
.
.
.
.
.
.
.
.
D2
F
F
F
U
R2
F
B’
Kociemba Two-Phase
Algorithm
Phase 1
43,252,003,274,489,856,000 possible starting orientations
All 18 possible moves are used
Uses pruning and symmetries
2,217,093,120 possible phase 1 solutions
Phase 1 Solution: F, U, F2, L2, U2, B2, L’, U, R2, F, B’ (11 moves)
U
F2
L2
U2
B2
L’
L

## Slide 11
U
D
U’
D’
B2
F2
R2
U2
L2
D2
.
.
.
.
.
.
.
D2
U
D’
R2
U’
F2
U
D
B2
Phase 2
2,217,093,120 possible starting orientations
A subset of 10 moves are used
Uses pruning and symmetries
1 possible phase 2 solution
U
U
R2
Phase 2 Solution: U, R2, D’, R2, U’, F2, U, D, B2 (9 moves)
Final Solution: F, U, F2, L2, U2, B2, L’, U, R2, F, B’, U, R2, D’, R2, U’, F2, U, D, B2 (20 moves)

## Slide 12: Mechanical Actuators
One arm for each face
Each arm must actuate, avoiding contact with the other arms
Initial design ideas:
  Rotary motion to linear motion
  Linear actuator motor
Solution: Double action pneumatic air cylinder
  High Speed
  Affordable
  Small footprint
Controlled by solenoid valve and a
relay board
Simultaneous coaxial pair motion
Approximately 80-100psi

## Slide 13: Electro-Mechanical Stepper Motors
Each actuating arm will have a stepper motor to rotate each face
90/180 degree rotations clockwise or counter-clockwise
Controlled by an FPGA and proprietary motor control board
Full steps, no micro-stepping
Break sensor for 90 degree
alignment.

## Slide 14: Summary
Integrates various technologies and domains of engineering.
  Computer and Electrical engineering combined with mechatronics and robotics
Great application of system integration and teamwork.
Mechanical components pose the greatest limitations.

## Slide 15: Acknowledgments
Point Grey Research
BioFire Defense
Futura Industries

## Slide 16: REFERENCES
[1] Guinness World Records. Fastest robot to solve a Rubik's Cube [Online]. Available: http://www.guinnessworldrecords.com/world-records/fastest-robot-to-solve-a-rubiks-cub
[2] OpenCV Developers Team. Miscellaneous Image Transformations [Online].
Available: http://docs.opencv.org/modules/imgproc/doc/miscellaneous_transformations.html#cvtcolor
[3] OpenCV Developers Team. Feature Detection [Online]. Available: http://docs.opencv.org/modules/imgproc/doc/feature_detection.html?highlight=canny#canny
[4] OpenCV Developers Team. Structural Analysis and Shape Descriptors [Online]. Available: http://docs.opencv.org/modules/imgproc/doc/structural_analysis_and_shape_descriptors.html?highlight=findcontours#findcontours
[5] Herbert Kociemba. The Two-Phase Algorithm [Online]. Available: http://kociemba.org/cube.htm